# Engine

Services / Major component types are registered with the service configuration. Upon application start the configuration is used to resolve and construct instances for each registered type. / During startup the configuration will automatically sort constructors and automatically inject referenced services. On shutdown the application will dispose each instance in reverse order of construction. / VideoContext takes the Window as constructor parameter. / ServiceConfiguration will sort Window before VideoContext. / Window instance is constructed / VideoContext is constructed with the current Window instance. / VideoContext will be disposed before Window. / User Input / Events are implemented via the MessageBus service. This service manages generic subscriptions and broadcasting. / Subscriptions are disposable objects that hold weak references to an instance of a specific interface. The MessageBus allows other components to broadcast function calls to all subscribers of an interface. / In regard to thread-safety, only the subscribe & unsubscribe operations will be synchronized. The implementation of a subscriber must then handle any additional synchronization if desired. / The application may register and observe any interface, which can be useful for handling game specific entities. At minimum the are 5 internal interfaces that deal with platform specific messages: / AudioDeviceListener Life time of audio devices. / VideoDeviceListener Life time of video device. / WindowListener Life time and update messages of the window. / KeyboardListener Keyboard input messages / MouseListener Mouse input messages	Rendering / Rendering is split into two different subsystems: Surface management and draw calls. / Surfaces are disposable handles to implementation specific images. When used for drawing, the video system will make sure that the latest version is uploaded to the output device before executing. / In order to draw a surface, the caller must specify a destination and source , tint color and effect flags. / Destination is a rectangle that defines the region of the output viewport that will be filled with the pixels. / Source is a rectangle that specifies the region of pixel data of the surface that is used to fill the destination. / Nearest neighbor is used to resolve size differences between destination and output. / Effect flags are fixed function manipulations that are executed before fetching the pixel data. / The pixel data of source is multiplied with the tint color before drawing. / Alpha blending is applied to the final result, before it's copied to the viewport: Surf.rgb * Surf.a + View.rgb * (1.0 – Surf.a) / Sound / Not implemented. / The library provides a set of instruments. / Application submits “tracks” to play the instruments.

# Views

Panels / Panels are generic views allows the game to display various child windows on top of the current game. At any point there can be only one child on the left and on on the right side of the screen. The party widget at the bottom allows the user to switch between characters. / Message Box / This view is used to notify the user about various events that occur wile playing. There can only be one active message box at any time, while the message box itself may display a number of different child views. / Message Boxes are is used to display popup windows for menus, random encounters or other important notifications.	Story / Cutscenes are handled with a single screen that displays some image and textbox widget. A list of buttons allows the user to navigate select different branches during the scene. / Dialog / This screen is used when talking to an NPC. On the left side a portrait is composed from a background and a sprite, while the right panel will display a text and buttons for available topics. The currently selected party member is used for skill checks that may occur during a dialog.

Inventory / The inventory is a left-side panel that implements a classic paper doll for equipment. The backpack displays all items that are currently not equipped by any party member. Selecting a different character will change the paper doll but the backpack is shared across the party. / Vendor / When selecting the “buy / sell” topic of a vendor, the game will display the inventory panel and a widget for the vendor that is similar to the backpack. This vendor widget contains a list of all the items that are currently up for sell. Buying and selling items works via right-click or drag & drop. In both cases an optional message box will be presented in order to handle further details like quantity, haggling etc..	Exploration / The exploration screen is shown while traveling the region or when entering locations on the map. The map is a visual representation of the game world that can be navigated via keyboard. Actions display a list of buttons that allow the user to trigger common tasks during travel or show management panels. / When entering a special location, the screen is basically the same except that different actions will be shown. In a settlement this could be a list vendors or NPCs, while a ruin in the wild may include options that trigger skill checks. / Combat / When combat is triggered the game will display the party on the left and all monsters on the right. An random background image is shown behind both for the current environment. / Once a party member is taking it's turn, the bottom panel becomes active and displays the buttons for all possible combat actions. Additional input (i.e. for selecting a spell) will be presented in a message box when necessary.

# Mechanics

World / The world is a two-dimensional array composed from cells, while each cell holds references to a region, terrain, feature and an optional location. / The primary function of terrain is to indicate how fast characters may travel through a given cell. Special talents may refer to the terrain in order to grant bonuses. / Regions are names that will be displayed when the user interacts with a cell. Quests may refer to the region in order to give a general sense of direction. / Features define tables for random encounters and the frequency for when encounters will be used.	Exploration / The exploration screen is shown